## Slide 1
EE216A – Project 2017
Team members
Sheng Yung Tao: 605033865
Zaurbek Tsorojev: 805029443

## Slide 2: Our results
Technology | Synopsys 32nm | hvt/wgt not reg | rvt/wgt reg
Core Area | Total cell area: Total area: | 1.127 mm² 2.432 mm² | 2.134 mm² 4.048 mm²
Power | Switch: Internal: Leakage: Total: | 8.91 mW 50.6 mW 0.225 W 0.28 W | 15.1 mW 46.3 mW 4.89 W 4.96 W
Clock Period |  | 2 ns | 2 ns
N clk cycles to process image |  | 408 | 408
Energy/Image | Ptot * Nclk * Tclk | 0.23 µJ | 4.05 µJ
Energy-Area Product | (µJ*mm²) | 0.55 | 16.39
First column of results is for high Vt and input weights not registered, the second is for regular Vt and registered input weights. We did not have enough time to run the last synthesis with high Vt, but from our analysis with the case wgt not reg at both rvt and hvt, we can assume it would have reduced the leakage power by an order of magnitude.
We were able to successfully synthesize our design and verify post synthesis with 100% accuracy (working of the design with .sdf).

## Slide 3: Optimization
We minimized the area by using a minimum number of blocks. Our final design has only 20 multipliers. Here is the diagram for one neuron.
Less blocks means less transistors and thus less leakage. We save on power and gain efficiency. We also used a high Vt in the synthesis of non-registered input weights, which significantly reduced leakage. (~10x)
We use pipelining (sequential flow – decreases area) and parallelism (10 neuron blocks in parallel – increases speed). Using both these methods together seem to give the best result.
We also added buffers to the clock and reset in order to decrease the fanout and thus decrease the delay.
M
M
A
A
A